## Slide 1: Anomaly detection and generation in time-series for predictive asset maintenance Final presentation 10th September 2019
Hitesh Kumar
Department of Earth Science and Engineering - Imperial College London
Data Science - Shell Research Limited

## Slide 2: Overview
Background on the problem
Data and EDA
Anomaly detection
Anomaly generation
Question time

## Slide 3: Background

## Slide 4: Some context first…
Compressors play a big part in natural gas extraction and processing.

## Slide 5: Some context first…
Input/output pressures, temperatures, flow rates and other variables change a lot during operation

## Slide 6: Some context first…
Input/output pressures, temperatures, flow rates and other variables change a lot during operation
So we have a m-dimensional multivariate time-series of length N

## Slide 7: Some context first…
But sometimes they behave badly, causing:
Efficiency reduction
Automated/manual shutdowns
Damage to parts
Financial losses (for everyone) + Health and safety risks

## Slide 8: Some context first…
So now we had our task; Multivariate time-series anomaly detection!
We split this into 3 sub-tasks
Find a way to detect anomalous intervals of time in our data-set
Predict the time until next anomalous event
Determine which features specifically are behaving anomalously/normally in said interval

## Slide 9: Data and EDA

## Slide 10: Our data-set
N = ~130,000 at 10 minute intervals (~2.5 years of data!)
M = 405, but only 227 from the actual compressor

## Slide 11: Our data-set
Lets look at time first:
Sometimes the compressor is offline

## Slide 12: Our data-set

## Slide 13: Our data-set
Lets look at time first:
Sometimes the compressor is offline
This is not “normal” behavior”
Get rid of it

## Slide 14: Our data-set
N = ~130,000 ~106,000
M = 405, but only 227 from the actual compressor

## Slide 15: Our data-set
Also, we observe the scale of the data changing really strangely at times…

## Slide 16: Our data-set

## Slide 17: Our data-set
Lets look at time first:
Also, we observe the scale of the data changing really strangely at times…
We have no idea what units it was changed to and from
We tried rolling window normalization, squashing (sigmoid, tanh etc.) and other stuff

## Slide 18: Our data-set
So we decided to instead take the differences between time-steps:

## Slide 19: Our data-set
Now the data looks like this

## Slide 20: Our data-set
And now in space:
There are some features which are just bad…

## Slide 21: Our data-set

## Slide 22: Our data-set
And now in space:
There are some features which are just bad…
So we came up with some criteria, get rid of any feature that:
  Has too many missing values overall
  Has too many consecutive missing values
  Has too low a variance (under review)
  Has Less than 2000 unique values
  Has too many consecutive 0’s (no change) (second part only)

## Slide 23: Our data-set
N = ~130,000 ~106,000 ~105,999
M = 227 112 (subject to decrease)
And finally we standardise this

## Slide 24: Our data-set
We need to create finite length sub-sequences out of this data

## Slide 25: Our data-set
Now we have ~1400 sequences of 144 time-steps each
Each consecutive sequence is 50% the same (maximum) due to a 72-timestep stride
No overlap in training/validation/test sets
9 anomalies at 144 timesteps each, focal point at center in time
PyTorch DataLoader!

## Slide 26: Anomaly detection

## Slide 27: Considerations
But now we have two issues:
There isn’t any easy way to measure how anomalous time-series are

## Slide 28: Considerations

## Slide 29: Considerations
But now we have two issues:
There isn’t any easy way to measure how anomalous time-series are
There are very few labelled anomalies in the data set

## Slide 30: Considerations
We only have 9 labelled anomalies: 9 points in time out of 130,000!
Even by expanding the windows to multiple days around each anomaly, we can only get 4428 points in total.
3%!

## Slide 31: Considerations
But now we have two issues solutions:
There isn’t any easy way to measure how anomalous time-series are – Deep Learning
There are very few labelled anomalies in the data set – Unsupervised
LSTM Auto-encoder

## Slide 32: Model and results
LSTM:

## Slide 33: Model and results

## Slide 34: Model and results
Mathematically:
Latent vectors

## Slide 35: Model and results
Reconstruction error:

## Slide 36: Model and results
So there are two things everyone expects from Auto-encoders:
Encoded latent vector projections – Encoding + PCA/TSNE

## Slide 37: Model and results

## Slide 38: Model and results
So there are two things everyone expects from Auto-encoders:
Encoded latent vector projections – Not so good
Reconstruction errors

## Slide 39: Model and results

## Slide 40: Model and results

## Slide 41: Model and results
Recon errors (loss function) could be 400x larger
No incentive to optimise for most features
Result is based on a few features only

## Slide 42: Model and results

## Slide 43: Model and results
So there are two things everyone expects from Auto-encoders:
Encoded latent vector projections – Not so good
Reconstruction errors – Pretty good

## Slide 44: Model and results
Now we just need to classify these reconstruction errors somehow
Look at reconstruction error distribution
Decide a threshold to balance FPs/FNs

## Slide 45: Model and results

## Slide 46: Model and results

## Slide 47: Model and results

## Slide 48: Model and results

## Slide 49: Model and results
Predicted Actual | True | False | Total
True | 1203 | 205 | 1408
False | 1 | 8 | 9
Total | 1204 | 213 | 1417

## Slide 50: Further work
Better data-preprocessing
More experiments with latent space and projections
Sample variance weighted loss function – More inclusive reconstructions

## Slide 51: Further work
Better data-preprocessing
More experiments with latent space and projections
Sample variance weighted loss function – More inclusive reconstructions
Time-dependent classification boundary

## Slide 52: Further work

## Slide 53: Further work
Better data-preprocessing
More experiments with latent space and projections
Feature variance weighted loss function – More inclusive reconstructions
Time-dependent classification boundary
Time-to-failure predictions based on reconstruction error time-series

## Slide 54: Anomaly generation

## Slide 55: Why do we need to generate data?
Why do we even need more data?

## Slide 56: Why do we need to generate data?
Perhaps we can get some success with supervised methods?
Reduce class imbalance
Train RNN-based direct classification models
Perhaps even direct time-to-failure models?...

## Slide 57: Why do we need to generate data?
...and would like to learn more about various types of anomalies…

## Slide 58: Why do we need to generate data?
…as well as new anomalies that are very rare or impossible.

## Slide 59: Considerations
We have a 3 step plan:
We have to be able to sample from the real data distribution
We need to post process a string of random samples into a realistic time-series
We need to figure out how to make “anomalous-looking” time-series
?
?
?

## Slide 60: Considerations
Step 1: Lets see the distribution first

## Slide 61: Considerations
98% of all data
1%
1%

## Slide 62: Considerations

## Slide 63: Considerations

## Slide 64: Considerations
- Essentially we want to create some mapping from samples from one distribution to another:

## Slide 65: Model and results
We tried some simple ideas…
Approximate the inverse CDF of the data
Kernel density estimation with bootstrapping
Maximum likelehood/Bayesian methods
But these require certain conditions/assumptions, and hard to scale

## Slide 66: Model and results
…But in the end we chose to go with
Generative adversarial networks (GANs)

## Slide 67: Model and results

## Slide 68: Model and results
Some that we implemented:
GAN
LSGAN
WGAN
WGAN + GP

## Slide 69: Model and results
The architecture (MLP):

## Slide 70: Model and results
We tested a few architectures:
- MLP
RNN

## Slide 71: Model and results
We tested a few architectures:
- MLP
RNN
Temporal convolutions

## Slide 72: Model and results
Some just didn’t work no matter what was tried:
- MLP - Some success
RNN - Some success
Temporal convolutions – No success

## Slide 73: Model and results
Details:
Multi-layer perceptron (4 linear layers) with LeakyReLU non-linearity
Learning independent, One-dimensional distribution of each feature separately
Latent space larger than output space (Generator)
Discriminator has around 100x capacity of generator
No Recurrent layers – Optimisation and loss has nothing to do with temporal dependencies
Keep step 1 as pure as possible – learn the distribution only

## Slide 74: Model and results

## Slide 75: Model and results
After a lot of experiments, went with LSGAN + generator weight decay

## Slide 76: Model and results
And got good results!

## Slide 77: Model and results
A = C = 1
B = 0
Gamma = 0.01

## Slide 78: Model and results
Applied weight decay to generator:
Much more stable and smooth convergence

## Slide 79: Model and results

## Slide 80: Model and results

## Slide 81: Model and results
Applied weight decay to generator:
Much more stable and smooth convergence
Very reliable convergence

## Slide 82: Model and results
Models Results | GAN | LSGAN | WGAN | WGAN + GP
JS-divergence | 0.089 | 0.0034 | 0.014 | 0.013
W-distance | 197.01 | 15.40 | 80.92 | 46.57

## Slide 83: Further work
So far we’ve only accomplished step 1…
We have to be able to sample from the real data distribution
  - Extend to multivariate distributions
We need to post process a string of random samples into a realistic time-series
We need to figure out how to make “anomalous-looking” time-series
But time was nearly up, so we had to git going

## Slide 84: Further work
But we have some plans:
PLAN 1:
Merge steps 1 and 2:
  Dual/Multi discriminator GANs
  Multi-objective recurrent GANs
What is a “real” time-series?

## Slide 85: Further work
Dynamic time warping (DTW)
Similarity measure between time series
No strong assumptions about the data (scale invariant)
SoftDTW – differentiable implementation

## Slide 86: Further work
But we have some plans:
PLAN 1:
Merge steps 1 and 2:
  Dual/Multi discriminator GANs
  Multi-objective recurrent GANs
Step 3:
  Randomly adding short-term large scale noise?
  LSTM post-processor
What is a “real” time-series?

## Slide 87: Further work
But we have some plans:
PLAN 2:
Step 1 remains same
Merge steps 2 and 3:
  De-noising auto-encoders
  Style transfer models

## Slide 88: Further work
Style transfer models

## Slide 89: Further work
Style transfer models

## Slide 90: Summary
Compressors are crazy
Real data is very messy – still not done cleaning
Anomaly detection shows some good first results – can be much improved
Anomaly generation has just started, and needs a lot more research
So much more can be done…